## Slide 1
Real-time/hindcast modelling system
Central Western Australia

## Slide 2
Australia

## Slide 3
Western Australia

## Slide 4
Complex topography
Higher res. along the coast
~ 2.5 km – 4 km
Smooth as little as possible for long run
  LP, iterative, point wise
Keep rx1 small (HPGE)
NDTFAST = 32, DT=120s
Perth 500 m child, DT=100s (!)
ROMS model setup CWA
DA is expensive (~ 30 x NLM)
  15 TLM/ADJ (back/forth)
Correcting atmo, ini, bc
DA with tides -- mixing, HF, many obs
Optimize for HPC
  Optimize the grid size 640x480
  IVEC Pawsey Magnus (Cray XC40)
  4hr wall clock for DA  4 day cycle

## Slide 5
Magnus Cray XC40
1488 nodes (35,712 cores)
2 x 2.6GHz E5-2690 v3 "Haswell”
Cray Aries interconnect Dragonfly
Cray Sonexion 1600 Storage
(3PB r/w 70GB/s)
LUSTRE FS using stripes -> DA
Magnus Pawsey HPC

## Slide 6
Parent/child nesting

## Slide 7
PLATFORM OBS
NOAA_15 297420 NOAA_16 588766 NOAA_18 734152 NOAA_19 699573 ROT_HF 117618
AVISO 4768 ADCP_WATR10 1536 ADCP_WATR20 2880 ADCP_WATR50 2880 ADCP_WACA20 2880 TZ_WACA20 3591 TZ_WACASO 5433 TZ_WATR10 3586 TZ_WATR20 3753 CTD_WATR20 1026
ARGO_R59 160
Data Assimilation: Observations
~ 2,5 million observations (4 day window from 21/Jan)
Notes: In total for 3 months I used ~ 30 mil of observations

## Slide 8
Data Assimilation: WA (4 days)

## Slide 9
Data Assimilation: WA (4 days)

## Slide 10
Data Assimilation: WA (3 months)

## Slide 11
Data Assimilation: WA (3 months)

## Slide 12
Data Assimilation: WA (3 months)
~30 million data points assimilated

## Slide 14
Real-time CWA/Perth system

## Slide 16
Real-time CWA/Perth system

## Slide 18
Real-time CWA/Perth system
HYCOM GL
nco tools

## Slide 19
GFS 0.25
nco tools
Real-time CWA/Perth system

## Slide 20
WRF – ARW
2-way nested 10 <-> 2 km
Hourly outputs
“TS” files 6s (like station files)
Automatically via cron
Python pre/post processing
  Make forcing
  Make plots
  Archive
  Serve via openDAP / ncWMS
Real-time CWA/Perth system

## Slide 21
ROMS – CWA
2-4 km, tilted and stretched
M2,S2,N2,K2,K1,O1,P1
HYCOM bry
WRF/GFS forcing
3-hourly & daily outputs
station file along the Perth bry (10min)
Automatically via cron
Python pre/post processing
  Make bry for child
  Make plots
  Archive
  Serve via openDAP / ncWMS
Real-time CWA/Perth system

## Slide 22
Real-time CWA/Perth system
ROMS
Perth 500m
parent bry @ 10min
WRF hourly forcing
1-hourly & daily outputs
station file (5min)
Automatically via cron
Python pre/post processing
  Make plots
  Archive
  Serve via openDAP / ncWMS

## Slide 23
Real-time CWA/Perth system
HYCOM
GFS 0.25
Python (seapy) + shell
WRF
10/2 km
ROMS bry
ROMS frc
ROMS
sta
ROMS bry
ROMS frc
ROMS
sta
GLOBAL MODELS

## Slide 24
Real-time CWA/Perth system

## Slide 29
Final thoughts
Specific problem should be addressed specifically (grid, smooth)
  One time investment, used many times
When planning modelling system, think of hardware
  Small grids run fast on the WS
Python can speedup gridding for DA
  using in parallel, fork time independent processes
  prepare bry, forcing, start model, plot …
DA using tides / not ?
  Tidal mixing, internal tides, bottom friction and bottom mixing
  No need for LP & mean state within assimilation (3DVar)
Data dissemination, openDAP, TDS, ncWMS, free software

## Slide 30
url=’http://130.95.29.59:8080/thredds/dodsC/realtime/agg_avg.ncml’
nc = netCDF4.Dataset(url)
lon_rho = nc.variables['lon_rho'][:]
lat_rho = nc.variables['lat_rho'][:]
temp= nc.variables[‘temp'][itime, -1, :, :]