## Slide 1
jwilkin@rutgers.edu http://marine.rutgers.edu/wilkin
Data Assimilative Modeling in Coastal and Shelf Waters of the U.S. Mid-Atlantic Bight and Gulf of Maine
John Wilkin
Julia Levin, Javier Zavala-Garay, Hernan Arango Marine and Coastal Sciences Rutgers, The State University of New Jersey
New Brunswick, NJ, USA
Regional Ocean Modeling System http://myroms.org
ROMS User Workshop, Hobart, Australia 17-20 October 2016

## Slide 2
Circulation of the Mid-Atlantic Bight (MAB) and Gulf of Maine (GOM)
Dynamics of the MAB shelf-break front

## Slide 3
http://maracoos.org
Mid-Atlantic Regional Association of Coastal Ocean Observing Systems
** it’s a double espresso
ESPreSSO* real-time and reanalysis ROMS system
*Experimental System for Predicting Shelf and Slope Optics
Doppio** real-time and reanalysis system
Notes: Much better. More on this later.
Nested in NWA

## Slide 4
Data streams Real-time Data source
Surface and boundary forcing:
72-hour forecast NAM 0Z cycle at 2 am EST NCEP NOMADS Grads DODS Server
USGS daily river flow available 11:00 EST waterdata.USGS.gov
MERCATOR 7-day forecast updated daily Mercator-ocean.fr
Assimilation data sets:
Regional CODAR hourly: 4-hour latency delay Rutgers TDS*
IOOS glider T,S (1 hour delay) Rutgers TDS and IOOS glider DAC
SST AVHRR passes 6-8 per day (2 hour delay) tds.maracoos.org (from U. Del.)
SST GOES, WindSat & AMSR-2 IR PFEG ERDDAP; NASA PO-DAAC
Jason-2, CryoSat, AltiKa along-track GDR RADS.tudelft.nl
SOOP XBT/CTD, Argo floats on GTS OSMC.noaa.gov using ERDDAP
XBT/CTD archive UK Met. Office
Gulf of Maine moorings NERACOOS
No …. NSF OOI Pioneer Array moorings and gliders
*THREDDS Data Server unidata.ucar.edu
Notes: Reanalysis runs on data sets that are largely available in near real time.
Building a real-time (quasi-operational) and reanalysis system in coordination is the best way to go.
Greater potential to build user base – which can leverage support for both development branches

## Slide 5
RU CODAR de-tided (harmonic analysis) and binned to 5km
  variance within bin & OI combiner expected u_err (GDOP) used for QC
    >> ROMS tide added to de-tided CODAR – so tide phase error does not enter cost function
IOOS glider T,S averaged to ~5 km horiz. and 5 m vertical bins
Satellite SST: bin to 5 km resolution
  AVHRR 6-8 passes per day; 3-hour GOES composites; AMSR-E/2 SST
  Have previously used daily SST OI combination of microwave and IR
Altimetry along-track 5 km bins from RADS
  With coastal altimetry corrections can use to ~40 m isobath
  MDT from 4DVAR on climatological observations: 3D T,S, velocity (moorings, Oleander vessel ADCP, CODAR), mean τwind
  No Dynamic Atmosphere Correction (DAC)
  Add ROMS harmonic tide to SLA; repeat obs. +/- 2 hours
USGS daily river flow is projected by MCA to un-gauged watersheds
Open boundary data from MERCATOR adjusted to remove bias (using 4DVAR climatological analysis on MOCHA and velocity data sets)
Data pre-processing flow for Doppio 4DVAR
Notes: Canada rivers!

## Slide 6
Data pre-processing flow for Doppio 4DAR real-time system
All times New York local (U.S. EST)

## Slide 7
AltiKa
Oct 1
Jason
Oct 2
AltiKa
Oct 2
Cryosat
Oct 1
Jason
Oct 3
Example of CODAR data after quality control, binning and decimation to a set of independent observations.
Example of along-track altimeter sea level anomaly data during a single 3-day analysis window.

## Slide 10
AVHRR
Geostationary
Microwave
Analysis on 20160417
Forecast from 20160412

## Slide 11
Output goes to THREDDS server Forecast Model Run Collection* (FMRC)
at tds.marine.rutgers.edu/thredds
*unidata.ucar.edu

## Slide 12
Forecast Model Run Collection (FMRC): Output from a single analysis and forecast

## Slide 13
Constant Forecast Offset: Every realization of a given date from all forecasts

## Slide 14
ESPreSSO SSH variability correlation improves with assimilation, and predicts variance in withheld observations from ENVISAT
Analysis skill for SSH
Correlation when no assimilation
Correlation after assimilation of SSH and SST
Correlation with ENVISAT SSH not assimilated

## Slide 15
satellite data only
with CODAR assimilation
satellite data only
with CODAR assimilation
Lagrangian forecast skill w.r.t. U.S. Coast Guard (SLDMB) drifters
Observed Forecast: with satellite data only
also with CODAR assimilation

## Slide 16
satellite data only
with CODAR assimilation
satellite data only
with CODAR assimilation
Median separation distance (error)
Observed Forecast: with satellite data only
also with CODAR assimilation
Addition of HF-radar (CODAR) to assimilation system gives modest error reduction, but more significant reduction in uncertainty (error bars are 5% and 95%)
Separation normalized by distance traveled
Lagrangian forecast skill w.r.t. U.S. Coast Guard (SLDMB) drifters

## Slide 17
days since 01-Jan-2006
Sub-surface T/S analysis and forecast skill
In situ T and S observations are not assimilated so offer independent skill assessment
There is a sizeable archive of observatory data from CTD, gliders and XBTs for 2006 (SW06) and 2007
7

## Slide 18
Analysis/forecast skill with respect to subsurface OBS that are NOT assimilated
Temperature
Forward model

## Slide 19
Analysis/forecast skill with respect to subsurface OBS that are NOT assimilated
Temperature
Forward model after bias removal

## Slide 20
Analysis/forecast skill with respect to subsurface OBS that are NOT assimilated
Temperature
Data assimilation analysis/hindcast
8

## Slide 21
Analysis/forecast skill with respect to subsurface OBS that are NOT assimilated
Temperature
2-day forecast

## Slide 22
Analysis/forecast skill with respect to subsurface OBS that are NOT assimilated
Temperature
4-day forecast
9

## Slide 23
RUEL
ENV
MAB
EcoMon
summer
winter
summer
Comparison to MARACOOS gliders and NMFS CTD surveys in 2010-2011
Multi-model skill assessment: 7 real time models of the Mid-Atlantic Bight
Notes: AUGV tracks (colored lines) and ECOMON CTD stations (+ symbols) in 2010-2011. Geographic sub-regions R1, R2 and R3 are shown by color shading. Timeline panel shows dates of observations grouped by project: Rutgers University Endurance Line (RUEL), New Jersey state environmental agencies (ENV), long range MARACOOS deployments (MAB), and NMFS stock assessment voyages (ECOMON). For each box on the timeline the central line color corresponds to a map track, and the background color the sub-region in which the vehicle was operating at that time. Dark and light grey shading on timeline indicates summer and winter, respectively.

## Slide 24
Multi-model Skill Assessment using Coastal Ocean Observing System Data
All analyses – with “DA”
  global: HYCOM, Mercator, NCOM
  regional: ESPreSSO, NYHOPS, UMassHOPS, COAWST
  climatology: MOCHA
Model | THREDDS URL | Resolution in MAB | Output interval | Surface forcing | Tides | Rivers | Assimilation method | Data
HYCOM | http://tds.hycom.org/thredds/dodsC/ glb_analysis.html | 7 km 10 z-levels in h<100m | Daily snapshots | NOGAPS | No | Monthly climatology | MVOI | SSH, SST, T/S profiles
NCOM | http://edac-dap.northerngulfinstitute.org/ thredds/dodsC/ncom_reg1_agg/NCOM_Region_1_Aggregation_best.ncd.html | 11 km 19 TF-levels in h<100m | 3-hour snapshots | NOGAPS | Yes | Monthly climatology | Weighted sum | SSH, SST, T/S profiles
MERCATOR | Register at myocean.eu. Python script motu-client.py used to access data set PSY2V4R2 | 7 km 12 z-levels in h<100m | Daily average | ECMWF | No | Monthly climatology | SEEK filter | SSH, SST, T/S profiles
NYHOPS | http://colossus.dl.stevens-tech.edu:8080/ thredds/dodsC/fmrc/NYBight/NYHOPS_ Forecast_Collection_for_the_New_York_Bight_best.ncd.html | 4 km 10 TF-levels | 10-min averages | NCEP NAM | Yes | Hydrologic forecast and point sources | None | N/A
ESPreSSO | http://tds.marine.rutgers.edu/thredds/ dodsC/roms/espresso/2009_da/his.html | 5 km 36 TF-levels | 3-hour snapshots | NCEP NAM | Yes | Daily observed | 4D-VAR | SSH, SST, CODAR
UMassHOPS | http://aqua.smast.umassd.edu:8080/thredds/ dodsC/pe_shelf_ass/fmrc/HOPS_PE_SHELF_ASS_Forecast_Model_Run_Collection_best.ncd.html | 15 km 16 TF-levels | Daily average | NCEP GFS | No | None | Feature model OI | SSH, SST
COAWST | http://geoport.whoi.edu/thredds/dodsC/ coawst_2_2/fmrc/coawst_2_2_best.ncd.html | 5 km 16 TF-levels | 2-hour snapshots | NCEP NAM | Yes | None | None | N/A
MOCHA climatology | http://tds.marine.rutgers.edu/thredds/ dodsC/other/climatology/mocha | 5 km 50 z-levels in h<100m | Monthly | N/A | N/A | N/A | Weighted least squares | T/S profiles

## Slide 25
MAB March 2010
Notes: Temperature (left) and salinity (right) versus along-track distance and depth for the MAB AUGV deployment of 04/2010 (see Fig. 1 for trajectory). Top row: reduced resolution observation set obtained following binning described in text. Other rows: Individual model results interpolated to the AUGV track at binned observation times. Model labels are as defined in Table 1. Summary line plots show root mean squared error (RMSE), mean bias (MB), centered root mean squared error (CRMS) and cross-correlation (R) versus depth for each model compared to this set of observations.

## Slide 26
Ensemble Mean BIAS (x-axis) and Centered RMS error (y-axis)
Distance from origin is Root Mean Squared Error (RMSE) Error bars are 95% conf.
Multi-model skill assessment
7
1
0.75
0.5
0.25
0
Centered RMS error
Mean BIAS
0 0.25 0.5 0.75 1

## Slide 27
7
Mean BIAS
1
0.75
0.5
0.25
0
Centered RMS error
0 0.25 0.5 0.75 1
Multi-model skill assessment
Ensemble Mean BIAS (x-axis) and Centered RMS error (y-axis)
Distance from origin is Root Mean Squared Error (RMSE) Error bars are 95% conf.

## Slide 28
Skill assessment
Vectors: 2-year mean surface current compared to CODAR
Color: Magnitude of vector complex correlation (for daily variability)
Notes: ESPreSSO assimilates CODAR COAWST assimilation=nudging
Next, GODAE models …

## Slide 29
Skill assessment
Vectors: 2-year mean surface current compared to CODAR
Color: Magnitude of vector complex correlation (for daily variability)
What next?
Observation impact

## Slide 30: Bias removal
Removing bias from boundary conditions and data is crucial
4D-Var will not converge if it cannot reconcile model and data error
Co-variances embodied in the Adjoint and Tangent Linear physics are incorrect if the background state is biased
Open Boundary Conditions (T and S) from HYCOM are adjusted by matching mean to regional climatology (MOCHA)
Open boundary sea level and velocity, and regional Mean Dynamic Topography (MDT) are computed using 4D-Var with annual mean observations (climatology)
Some details …

## Slide 31
Bias in global data assimilating models compared to a regional climatology:
Data (obs. number) sorted by ocean depth in model domain
-2 0 2 oC
-1 0 1 oC
Bias is problematic for down-scaling
HYCOM minus Observed oC
MERCATOR minus Observed oC
Notes: Downscaling is hampered by bias in large scale analysis fields.

## Slide 32
Combine …
High-res regional T/S
climatology (MOCHA)
with …
4DVAR analysis of mean climatological ocean state

## Slide 33
velocity obs. from … surface drifters moorings (blue, green)
and ship ADCP (magenta) ) CODAR (red)
… to get ... >>
4DVAR analysis of mean climatological ocean state

## Slide 34
Mean Dynamic Topography (MDT) in meters from ROMS climatological 4DVAR
4DVAR analysis of mean climatological ocean state
… a dynamically and kinematically adjusted MDT, and seasonal T,S,u,v for OBC bias removal

## Slide 36
Lentz (JPO, 2008)
100 m

## Slide 37
Summary
Rutgers ROMS ESPreSSO and Doppio 4DVAR use all available data from a modern coastal ocean observing system
  Satellite SSH and SST, HF-radar, gliders, Argo, GTS XBT/CTD
  More and diverse data is better
  Pre-processing for QC; tides in altimetry; binning to independent obs.
  OBC bias removal essential: use mean state from 4DVAR-based climatology
  Data ingest and output exploits web services (OPeNDAP/THREDDS) and interoperability of data conventions (CDM, CF-conventions, NetCDF/HDF)
Useful skill for real-time applications
  4 days for temperature and salinity; 1-2 days for velocity
Output of full model solution to THREDDS/FMRC Forecast Model Run Collection
  Surface currents to U.S. Coast Guard; Bottom temperatures to NOAA Fisheries
Development path
  Observation Impact analysis using variational tools
  Nesting (with 4DVAR)
  Representer-based observing system design/operation (for OOI Pioneer)
ROMS User Workshop, Hobart, Australia 17-20 October 2016